## Slide 1: AirNet Company Network Design & Security
Computer Networks Project
Using VLSM, VLANs, VPN & Security Controls
Group Members
Ali Raza (243749)
Waseem Abbas (243742)
M. Anas Akram (243766)
Mohsin Abbas (243743)

## Slide 2: Introduction
AirNet Company is a growing Australian enterprise
Head Office in Sydney with international branches
Requires secure, scalable, and efficient networking
Design focuses on security, performance, and future growth

## Slide 3: Business & User Requirements
Sydney HQ: 5000 users
Melbourne: 3200 users
Brisbane: 2500 users
Hong Kong: 2785 users
Reliable inter-branch communication required

## Slide 4: Networking Requirements
Private IPv4 block: 188.42.0.0/16
Secure Firewall connectivity between branches
Centralized services at Sydney HQ
VLAN-based departmental separating
Secure wired and wireless access

## Slide 5: Network Topology Selection
Hierarchical Star Topology selected
Widely used in enterprise environments
Easy scalability
Cost-effective and centrally managed

## Slide 6: Topology Architecture

## Slide 7: LAN Design Overview
Each building has 8 floors
Access switches on every floor
Distribution layer uses Layer 3 switches(Multi-layer switch)
Dedicated server room on Level 5
Firewall placed between LAN and Internet

## Slide 8: IP Addressing & VLSM
Base network: 188.42.0.0/16
VLSM used to avoid IP wastage
Subnets allocated from largest to smallest
Supports current users and future expansion

## Slide 9: Subnet Allocation Summary
Sydney HQ: 188.42.0.0/19 (8190 hosts)
Melbourne: 188.42.32.0/20 (4094 hosts)
Hong Kong: 188.42.48.0/20 (4094 hosts)
Brisbane: 188.42.64.0/21 (2046 hosts)
Efficient and justified allocation
Location | Network Address | CIDR | Subnet Mask | Usable IP Range
Sydney HQ | 188.42.0.0 | /19 | 255.255.224.0 | 188.42.0.1 – 188.42.31.254
Melbourne | 188.42.32.0 | /20 | 255.255.240.0 | 188.42.32.1 – 188.42.47.254
Hong Kong | 188.42.48.0 | /20 | 255.255.240.0 | 188.42.48.1 – 188.42.63.254
Brisbane | 188.42.64.0 | /21 | 255.255.248.0 | 188.42.64.1 – 188.42.71.254

## Slide 10: VLAN Design & Segmentation
VLAN 10 – Management
VLAN 20 – Human Resources
VLAN 30 – Finance
VLAN 40 – IT Support
VLAN 50 – Guest Network
VLAN 60 – Server VLAN (Level 5)

## Slide 11: Inter-VLAN Routing & Server Security
Inter-VLAN routing via Layer 3 switches
Server VLAN isolated for security
Only authorized VLANs allowed server access

## Slide 12: Hardware Selection & Wireless Network
Wireless networks can be easily expanded without the need for additional wires.
Layer 3 switches for high-speed routing
Layer 2 switches for access layer connectivity
Cat6 cabling for high performance

## Slide 13: Conclusion
Secure and scalable enterprise network designed
Efficient IP utilization using VLSM
Strong security using VLAN and firewalls
Design supports future business growth

## Slide 14: Thank You